## Slide 1: 兼容ARM9的软核处理器RTL设计
李新兵(risclite@gmail.com)
2012.04.21

## Slide 2: 兼容ARM9处理器架构
rom_en
rom_addr
第一级：取指
第二级：执行一
第三级：执行二
第四级：回写
code_flag
code
cmd_flag
cmd
Rm
Rs
sec_operand
Rn
to_vld
to_num
cha_vld
cha_num
go_vld
go_num

## Slide 3: 兼容ARM9软核处理器的接口
类别 | 名字 | 方向 | 位宽 | 描述
系统接口 | clk | IN | 1 | 时钟输入端口
 | rst | IN | 1 | 异步复位端口，高电平有效
 | cpu_en | IN | 1 | 同步使能端口，高电平有效
中断源 | cpu_restart | IN | 1 | ARM架构reset中断源，高有效
 | fiq | IN | 1 | ARM架构FIQ(fast interrupt)中断源，高有效
 | irq | IN | 1 | ARM架构IRQ(interrupt)中断源，高有效
 | rom_abort | IN | 1 | ARM架构Prefetch Abort(instruction fetch memory abort)中断源，高有效
 | ram_abort | IN | 1 | ARM架构Data Abort(data access memory abort)中断源，高有效
指令池接口 | rom_en | OUT | 1 | ROM读使能，高有效
 | rom_addr | OUT | 32 | ROM地址总线
 | rom_data | IN | 32 | ROM读数据
数据池接口 | ram_cen | OUT | 1 | RAM使能信号，高有效
 | ram_wen | OUT | 1 | RAM写使能信号，高电平代表写，低电平代表读
 | ram_addr | OUT | 32 | RAM地址总线
 | ram_rdata | IN | 32 | RAM读数据总线
 | ram_wdata | OUT | 32 | RAM写数据总线
 | ram_flag | OUT | 4 | RAM各字节使能信号

## Slide 4: 指令池模型与波形
指令池模型
clk
rom_en
rom_addr
rom_data
CLK
EN
ADDR
DOUT
rom_abort
ABORT
rom_addr
clk
rom_en
地址A
地址B
指令A
错误指令B
rom_data
rom_abort

## Slide 5: 数据池模型
数据池模型
clk
ram_cen
ram_wen
ram_addr[31:0]
ram_wdata[31:0]
ram_rdata[31:0]
CLK
CEN
WEN
ADDR
DIN
DOUT
BYTE_ENABLE
ram_flag[3:0]
ABORT
ram_abort

## Slide 6: 数据池模型访问波形
clk
ram_cen
ram_wen
ram_flag
4’b1111
4’b1100
4’b0010
ram_addr
地址A
地址B
地址C
ram_wdata
写数据A
N/A
N/A
4’b1111
地址D
N/A
半字B
字节C
错误字D
ram_abort
ram_rdata
字写
半字读
字节读
字读

## Slide 7: 第一级：取指的实现
取指阶段包含两个信号：rom_en与rom_addr
assign rom_en = cpu_en & ( ~(int_all | to_rf_vld | cha_rf_vld | go_rf_vld | wait_en | hold_en ) );
assign rom_addr = rf;
rf即PC(R15)

## Slide 8: 第一级rom_en
int_all: 发生任何中断，不用继续取指
to_rf_vld: to_vld对PC有效，此时跳转
cha_rf_vld: LDR指令写PC(第三级)
go_rf_vld: LDR指令写PC(第四级)
wait_en: 数据冲突的标志
hold_en: 多周期指令执行的标志

## Slide 9: 第二级的code_flag
always @ ( posedge clk or posedge rst )
if ( rst )
code_flag <= #`DEL 1'd0;
else if ( cpu_en )
if ( int_all | to_rf_vld | cha_rf_vld | go_rf_vld | ldm_rf_vld )
code_flag <= #`DEL 0;
else
code_flag <= #`DEL 1;
else;

## Slide 10: 第二级的乘法完成移位
寄存器组
code_is_xxx
code_rma
code
code_rm
code_rsa
code
code_rot_num
1’b1<<code_rot_num
mult_ans
reg_ans
code_rs

## Slide 11: 第二级的Rm
always @ ( *)
if ( code_is_ldrh1|code_is_ldrsb1|code_is_ldrsh1 )
code_rm = {code[11:8],code[3:0]};
else if ( code_is_b )
code_rm = {{6{code[23]}},code[23:0],2'b0};
else if ( code_is_ldm )
case( code[24:23] )
2'd0 : code_rm = {(code_sum_m - 1'b1),2'b0};
2'd1 : code_rm = 0;
2'd2 : code_rm = {code_sum_m,2'b0};
2'd3 : code_rm = 3'b100;
endcase
else if ( code_is_ldr0 )
code_rm = code[11:0];
else if ( code_is_msr1|code_is_dp2 )
code_rm = code[7:0];
else if ( code_is_multl & code[22] & code_rma[31] )
code_rm = ~code_rma + 1'b1;
else if ( ( (code[6:5]==2'b10) & code_rma[31] ) & (code_is_dp0|code_is_dp1|code_is_ldr1) )
code_rm = ~code_rma;
else
code_rm = code_rma;

## Slide 12: 第二级的Rs
always @ ( *)
if ( code_is_multl )
if ( code[22] & code_rsa[31] )
code_rs = ~code_rsa + 1'b1;
else
code_rs = code_rsa;
else if ( code_is_mult )
code_rs = code_rsa;
else begin
code_rs = 32'b0;
code_rs[code_rot_num] = 1'b1;
end

## Slide 13: 第二级的乘法结果
assign mult_ans = code_rm * code_rs;
always @ ( posedge clk or posedge rst )
if ( rst )
reg_ans <= #`DEL 64'd0;
else if ( cpu_en )
if ( ~hold_en )
reg_ans <= #`DEL mult_ans;
else if ( cmd_is_ldm )
if ( cmd_sum_m==5‘b1 )
reg_ans[6:2] <= #`DEL sum_m;
else if ( cmd[23] )
reg_ans[6:2] <= #`DEL reg_ans[6:2] + 1‘b1;
else
reg_ans[6:2] <= #`DEL reg_ans[6:2] - 1‘b1;
else;
else;

## Slide 14: 第三级的cmd_flag
always @ ( posedge clk or posedge rst )
if ( rst )
cmd_flag <= #`DEL 1'd0;
else if ( cpu_en )
if ( int_all )
cmd_flag <= #`DEL 0;
else if ( ~hold_en )
if ( wait_en | to_rf_vld | cha_rf_vld | go_rf_vld )
cmd_flag <= #`DEL 0;
else
cmd_flag <= #`DEL code_flag;
else;
else;

## Slide 15: 第三级的加法运算
reg_ans[63:0]
sec_operand
寄存器组
rna ([15:12]）
rnb ([19:16])
rn_register
rn
ALU
dp_ans
sum_rn_rm

## Slide 16: 第三级的加法器
assign sum_middle = add_flag ? ( rn[30:0] + sec_operand[30:0] + extra_num ) : ( rn[30:0] - sec_operand[30:0] - extra_num );
assign cy_high_bits = add_flag ? ( rn[31] + sec_operand[31] + sum_middle[31] ) : ( rn[31] - sec_operand[31] - sum_middle[31] );
assign bit_cy = cy_high_bits[1];
assign high_bit = cy_high_bits[0];
assign bit_ov = bit_cy ^ sum_middle[31];
assign sum_rn_rm = {high_bit,sum_middle[30:0]};

## Slide 17: 第三级的to_vld/to_num
assign to_vld = cmd_ok & ( cmd_is_mrs|((cmd_is_dp0|cmd_is_dp1|cmd_is_dp2)&(cmd[24:23]!=2'b10))|cmd_is_mult|cmd_is_multl|cmd_is_multlx|((cmd_is_ldrh0|cmd_is_ldrh1|cmd_is_ldrsb0|cmd_is_ldrsb1|cmd_is_ldrsh0|cmd_is_ldrsh1|cmd_is_ldr0|cmd_is_ldr1)&( cmd[21]| ~cmd[24]))|(cmd_is_ldm &(cmd_sum_m==5'b0)&cmd[21]) );
always @ (*)
if (cmd_is_mrs|(cmd_is_dp0|cmd_is_dp1|cmd_is_dp2)|cmd_is_multl)
to_num = cmd[15:12];
else
to_num = cmd[19:16];

## Slide 18: 第三级的cha_vld/cha_num
always @ ( *)
if ( cmd_ok )
cha_vld = (( cmd_is_ldrh0|cmd_is_ldrh1|cmd_is_ldrsb0|cmd_is_ldrsb1|cmd_is_ldrsh0|cmd_is_ldrsh1|cmd_is_ldr0|cmd_is_ldr1 ) & cmd[20])|cmd_is_swp;
else
cha_vld = 0;
always @ ( cmd )
cha_num = cmd[15:12];

## Slide 19: 第四级的go_vld/go_num
always @ ( posedge clk or posedge rst )
if ( rst )
go_vld <= #`DEL 1'd0;
else if ( cpu_en )
go_vld <= #`DEL cha_vld;
else;
always @ ( posedge clk or posedge rst )
if ( rst )
go_num <= #`DEL 4'd0;
else if ( cpu_en )
go_num <= #`DEL cha_num;
else;

## Slide 20: 寄存器组的写入
always @ ( posedge clk or posedge rst )
if ( rst )
r0 <= #`DEL 32'd0;
else if ( cpu_en )
if ( ldm_vld & ( ldm_num==4'h0 ) )
r0 <= #`DEL ldm_data;
else if ( go_vld & (go_num==4'h0) )
r0 <= #`DEL go_data;
else if ( cmd_ok & to_vld & ( to_num== 4'h0 ) )
r0 <= #`DEL to_data;
else;
else;

## Slide 21: 谢谢 问答